## Slide 1: Predictive Flow Scheduling using Deep Learning
ELAHEH JALALPOUR

## Slide 2: Outline
Introduction
Dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 3: Outline
Introduction
Dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 4: Flow Scheduling
Wide area network bandwidth
Constrained
Expensive
We want to maximum link utilization
Example: WAN bandwidth inter-datacenter network

## Slide 5: Flow Scheduling
  Traffic flow
  A stream of packets coming from a source towards a destination
  Sharing a link among the traffic flows
  The aggregate rate of flows can be bigger than the capacity of the shared link
  An scheduler controls the rate at the traffic source using rate limiters
A
B
C
Shared Link
D
E
RL
RL
RL
RL
Rate Limiter
Scheduler
The goal is to share the link among the flows to achieve maximum link capacity utilization

## Slide 6: Flow Scheduling – Continue
Subject to:
Shared Link
Link Capacity
Bandwidth utilization of flow
Allocated bandwidth to flow

## Slide 7: Challenges
The bandwidth utilization of flows are unknown ( is unknown)
Subject to:

## Slide 8: Outline
Introduction
Dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 9: Dataset
Collected traffic from a real environment
The traffic over a single link
Start-Time | Duration | Total-Bytes | Source-Address | Source-Port | Destination-Address | Destination-Port

## Slide 10: Dataset
Normalized between 0 and 1 as input
Chart: 

## Slide 11: Outline
Introduction
Dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 12: Why Deep Learning?
Knowing the traffic pattern can lead to better flow scheduling

## Slide 13: Why Deep Learning?
Traffic in the inter-DC networks often has a periodic pattern over time. Hourly/Daily
There is no unique traffic model to explain all traffic behavior
Some of traffic models
Poisson distribution
Pareto distribution process
Markov and embedded Markov models
Y. Li, H. Liu, W. Yang, D. Hu and W. Xu, "Inter-data-center network traffic prediction with elephant flows," NOMS 2016 - 2016 IEEE/IFIP Network Operations and Management Symposium, Istanbul, 2016, pp. 206-213

## Slide 14: Why Deep Learning?
Traffic types
Interactive services
Elastic services
Background services
Notes: We have three types of traffics in inter-dc networks:
Interactive services are in the critical path of end user experience
  one DC contacts another in the process of responding to a user request
  highly sensitive to loss and delay
Elastic services are not in the critical path of user experience
  replicating a data update to another DC
  requires delivery within a few seconds or minutes
Background services conduct maintenance activities
  copying all the data of a service to another DC
  bandwidth hungry
  it has no explicit deadline or a long deadline

## Slide 15: Outline
Introduction
Dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 16: Our Solution
Application of deep learning to
Predict traffic behavior
Schedule network flows
Utilizing the the traffic prediction to schedule network flows

## Slide 17: Predict Traffic Behavior
LSTM to learn the traffic pattern
Techniques
LSTM for Regression Using the Window Method
  Multiple, recent time steps are used to make the prediction for the next time step
  Phrasing the past observations as separate input features
LSTM for Regression with Time Steps
  Using the past observations as time steps of one input feature

## Slide 18: Train LSTM for Traffic Prediction
LSTM neural network
  input : 100 time step traffic volumes
  output : next step traffic volume
Hyper-parameters:
  learning rate: 0.001
  batch-size: 10

## Slide 19: Results of Traffic Prediction

## Slide 20: Results of Traffic Prediction

## Slide 21: Scheduling Network Flows
Using Reinforcement learning to schedule network flows
Input: Bandwidth demands of flow in the last timestamp
Output: Bandwidth allocation to each flow
Reward: Link utilization

## Slide 22: Reinforcement Learning for Flow Scheduling
Techniques
Vanilla policy-gradient
  One reward signal at the end of a long episode
  Does not work for continuous action space
Actor-critic policy-gradient

## Slide 23: Actor Critic Policy Gradient (DDPG)
  Approximate both the value function and the policy
  Model-free
  Off-policy
  Replay buffer
Notes:   approximate both the value function and the policy
  model-free
    make no effort to learn the underlying dynamics that govern how an agent interacts with the environment
  off-policy
  use another network the same as policy and update it every T second
  Replay buffer
  store experiences <state,action,reward,next state> in a buffer and sample minibatches from it to train the network

## Slide 24: Train and Testing DDPG
Hyper-parameters
Step per episode = 200
Learning rates
  Actor: 0.001
  Critic: 0.0001
Baseline
Greedy algorithm :
increase the allocation by a

## Slide 25: Results of Flow Scheduling

## Slide 26: Step three (In progress)
One agent for each flow group
Input: [link wastage of the last timestamp, total demand of the flow group in the last time stamp, total utilization of the flow group]
Output: prediction of the demand of the flow group
Reward: difference between the demand and the utilization ( penalize)

## Slide 27: Future work
Add more features for the flow groups
separate different flow group’s behavior by giving ports and ips as embedded features
the actual ip and port numbers does not have any correlation, embedding form of them shows their relations

## Slide 28: Outline
Introduction
dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion

## Slide 29: Related work
Job Scheduling in compute clusters
  SJF(shortest job first)
  Tetris scheduling heuristic [1]
  DeepRM [2] – a deep learning approach
  Agent learn interesting strategies like leave space empty for
future small jobs
[1] Robert Grandl, Ganesh Ananthanarayanan, Srikanth Kandula, Sriram Rao, and Aditya Akella. 2014. Multi-resource packing for cluster schedulers. SIGCOMM Comput. Commun. Rev. 44, 4 (August 2014), 455-466. DOI: https://doi.org/10.1145/2740070.2626334
[2] Hongzi Mao, Mohammad Alizadeh, Ishai Menache, and Srikanth Kandula. 2016. Resource Management with Deep Reinforcement Learning. In Proceedings of the 15th ACM Workshop on Hot Topics in Networks (HotNets '16). ACM, New York, NY, USA, 50-56. DOI: https://doi.org/10.1145/3005745.3005750

## Slide 30: Outline
Introduction
dataset
Deep learning as solution
Implementation and Evaluation
Related Work
Conclusion