## Slide 1: Deep Learning Applications for Atrial Fibrillation Detection in ECG Signals
By: Sara Ross-Howe
CS 898

## Slide 2: Agenda
Atrial Fibrillation (AFIB) – Definition, Characterization, and Real-World Impact of this condition
Traditional Biomedical Signal Analysis Approaches to AFIB Detection
Deep Learning Classification Models
  Autoencoders
  LSTM Network
  Convolution Network
Summarize Classification Results
Next Steps

## Slide 3: Atrial Fibrillation
Definitions
  Cardiac arrhythmia that is characterized by rapid and irregular ventricular beats.
  Instead of impulses originating directly from the Sinus Node, they initiate from multiple sites in the Atria, resulting in a chaotic heart rhythm.
  Estimated to cause 1 in 3 strokes for people over the age of 60 (https://www.heartandstroke.ca/heart/conditions/atrial-fibrillation)
  This condition contributes to an estimated 130,000 deaths each year in the United States (https://www.cdc.gov/dhdsp/data_statistics/fact_sheets/fs_atrial_fibrillation.htm)
          http://www.mayoclinic.org/diseases-conditions/atrial-fibrillation/symptoms-causes/dxc-20164936

## Slide 4: Atrial Fibrillation
Key Characteristics
  Irregular heart beat with increased R Peak-Peak variability
  Absence of a P-Wave before QRS complex
  Elevated ventricular rate >100 beats per minute
      https://en.wikipedia.org/wiki/Atrial_fibrillation
P-Wave
QRS Complex
T-Wave

## Slide 5: Atrial Fibrillation – Types
Paroxysmal: Self terminating within 7 days or episodes that are cardioverted within 7 days.
Persistent: Last for longer than 7 days and are terminated by either drugs or electrical cardioversion.
Long-Standing: Lasting ≥ 1 year and this is often the threshold for more aggressive rhythm control strategy.
Permanent: Long standing Atrial Fibrillation were rhythm control strategies are not being pursued.
http://www.doctoryg.com/2016/10/types-of-atrial-fibrillation.html?spref=pi

## Slide 6: Cloud DX – Biomedical Technology
Goal is non-invasive AFIB detection and monitoring in the home
      www.clouddx.com

## Slide 7: Quality Metrics
Sensitivity = Recall =
Specificity =
Precision =
Accuracy =
 | Disease Positive | Disease Negative
Test Positive |  | 
Test Negative |  | 
False Positive
True Positive
False Negative
True Negative

## Slide 8: Traditional Biomedical Signal Analysis Approaches to AFIB Detection
Tateno and Glass - Automatic detection of atrial fibrillation using the coefficient of variation and density histograms of RR and ARR intervals - McGill University - 2001
  Used the Komolgorov-Smirnov test based on cumulative distributions of ΔRR intervals from reference intervals from the MIT-BIH atrial fibrillation database
  Sensitivity: 93.2% and Specificity: 96.7%
  https://pdfs.semanticscholar.org/9509/63148f853e0239840ba40bf763e2de24ab37.pdf
Zhou et. al. - Automatic online detection of atrial fibrillation based on symbolic dynamics and Shannon entropy
  Used symbolic dynamics to describe Δ RR n and then Shannon entropy is calculated on the symbolic sequence to determine if the beat represents AFIB.
  Training - Sensitivity: 96.72% and Specificity 95.07%
  Testing on MIT-BIH AFIB database – Sensitivity: 96.89%, Specificity: 98.25%, Accuracy: 97.67%
  https://biomedical-engineering-online.biomedcentral.com/articles/10.1186/1475-925X-13-18

## Slide 9: Traditional Biomedical Signal Analysis Approaches to AFIB Detection
Annavarapu and Kora - 2016 - ECG-based atrial fibrillation detection using different orderings of Conjugate Symmetric–Complex Hadamard Transform
  Used a Hadamard transform to extract features for a Levenberg-Marquardt Neural Network (LMNN) classifier (20 input neurons, 10 neurons in hidden layer, and 3 neurons in the output). Trained on 1800 ECG beats and tested on 1006 ECG beats
  Sensitivity: 99.97%, Specificity: 98.7%, and Accuracy: 99.5%
  http://www.sciencedirect.com/science/article/pii/S2405818116300538

## Slide 10: PhysioNet – MIT-BIH AFIB Database
25 patient recordings of 10 hour duration
250 Hz sampling frequency with 12-bit resolution over a range of ±10 millivolts
Captured using ECG ambulatory recorders at Boston's Beth Israel Hospital (now the Beth Israel Deaconess Medical Center)
Annotated by manual identification of ECG beats as Atrial Fibrillation, Atrial Flutter, AV Junction Rhythm, or Normal Sinus Rhythm (all others)
https://physionet.org/physiobank/database/afdb/

## Slide 11: PhysioNet – MIT-BIH AFIB
Rhythm | Hours | Episodes | Beats
Atrial Fibrillation | 94.99 | 319 | 532,276
Atrial Flutter | 1.98 | 40 | 16,563
Other Rhythms | 163.03 | 293 | 733, 550
Total | 260.00 | 652 | 1,282,369
Most recordings represent paroxysmal atrial fibrillation events

## Slide 12: ECG Data Preparation
Human heart beat range 40 bpm – 200 bpm
Five second analysis window 3.33 beats – 16.67 beats
1 second stride
Balanced AFIB samples for each patient with NSR (plus other cardiac arrhythmias).
Lead I configuration was used
Samples are given a binary classification of AFIB if any beats in the region represent the arrhythmia.

## Slide 13: ECG Signal Pre-Processing
Fundamental signal preprocessing was done to the data before segmentation into training and testing sets.
60 Hz Notch Filter used to remove the electromagnetic interference (EMI)
Moving average subtraction was used to correct the baseline drift for DC offset (
Motion artifact
DC Offset Baseline Wander

## Slide 14: ECG Training and Testing Data Sets
Patient Recording | AFIB Samples | NSR (other arrhythmias) Samples | Total Training Samples | Total Testing Samples
04015 | 190 | 190 | 380 | 162
04043 | 5834 | 5834 | 11668 | 4998
04048 | 278 | 278 | 556 | 236
04126 | 989 | 989 | 1978 | 846
04746 | 12071 | 12070 | 24141 | 10344
04908 | 2186 | 2186 | 4372 | 1872
04936 | 7055 | 7054 | 14109 | 6046
05091 | 89 | 89 | 178 | 74
05121 | 9458 | 9457 | 18915 | 8106
05261 | 376 | 376 | 752 | 320
06426 | 1109 | 1108 | 2217 | 950
06453 | 282 | 282 | 564 | 240
06995 | 12164 | 12164 | 24328 | 10426
07162 | 0 | 0 | 0 | 0
07859 | 0 | 0 | 0 | 0
07879 | 10225 | 10224 | 20449 | 8764
07910 | 4123 | 4123 | 8246 | 3534
08215 | 4998 | 4997 | 9995 | 4282
08219 | 5702 | 5702 | 11404 | 4886
08378 | 5406 | 5406 | 10812 | 4632
08405 | 7158 | 7157 | 14315 | 6134
08434 | 1008 | 1008 | 2016 | 862
08455 | 7940.5 | 7940.5 | 15881 | 6804
Subtotal |  |  | 197276 (70.01%) | 84518 (29.99%)
Hours |  |  | 273.99 Hours | 117.39 Hours
Total |  |  | 281794 Samples | 391.38 Hours

## Slide 15: Autoencoders
Autoencoder is an unsupervised learning algorithm, where Xi represents both the input and output label Yi
Backpropagation is applied to learn an output function where
Minimize the reconstruction error - Loss(x) =
X1
B1
X2
X3
X4
Y1
B1
Y2
4
Hw,b(x)
http://ufldl.stanford.edu/tutorial/unsupervised/Autoencoders/
3
2
1

## Slide 16: Autoencoders - Variations
  Vanilla Autoencoder
    Basic format where train an output function such that
    Loss(x) =
    Layers are incomplete, thus forcing the network to
    compress the input
  De-noising autoencoder (DAE)
    = Xi + Zi ~ N(Xi,N)
  Variational Auto Encoder (VAE)
    A stochastic model of inputs, hidden units, and output
    L(ϕ,θ;x)=Ez∼qϕ(z|x)[log(pθ(x|z))]−DKL(qϕ(z|x)||pθ(z))
    Loss function = Reconstruction loss + regularizer term
    (Kullback-Leibler divergence)
    http://blog.fastforwardlabs.com/2016/08/22/
    under-the-hood-of-the-variational-autoencoder-in.html

## Slide 17: Autoencoders - Variations
  Sparse autoencoder
    Hidden layer over-represents the input and penalty terms are used to encourage sparcity during training.
    This can be achieved by removing weights
    Loss(x) = + λ
      Reconstruction loss is added to a sparcity term
  Convolution autoencoder
    Use convolution filter banks and pooling layers to generate feature maps

## Slide 18: Autoencoders
X1
X2
X3
X4
…
X247
X248
X249
X250
X1
X2
X3
X4
…
X247
X248
X249
X250
Y1
Y2
…
Y124
Y125
Z1
Z62
…
X124
X125
Encoder Layer 1
Encoder Layer 2
Decoder Layer 3
Decoder Layer 4
Incomplete/Contractive hidden layers
Stacked with 2 encoding layers

## Slide 19: Autoencoders - Results
Reference Versus Decoded Output – Layer 1
Reference Versus Decoded Output Layer 2

## Slide 20: Autoencoder – Reconstruction Loss
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Training | 0.12673 | 0.017056 | 0.0012251 | 0.00092478 | 0.0008894 | 0.0031104 | 0.0025178 | 0.0024472 | 0.0024191 | 0.0024037

## Slide 21: Autoencoders - Challenges
Signal Baseline
Weighted Average of All Inputs

## Slide 22: Autoencoders - Encoding
Sample Encoded Signals

## Slide 23: Autoencoders – Lessons Learned
Tie the output weights by using the transpose of the encoder for the decoder layer
Smaller input signal window better than larger ones
Initialize the network weights to small values in proportion to the nodes in the layer with (min , max )
Reduce the layer sizes by ~1/2 nodes of the previous layer
Use the Adam Optimizer (https://arxiv.org/abs/1412.6980)
Use layer-wise training
Use a smaller batch size (32) for increased accuracy but longer training times
Use shuffle batch with 100*batch size for capacity
Utilize more patient data to ensure variability and/or additive gaussian noise to the inputs.
Use Tanh as the activation function
Ensure the data is normalized to efficiently use the -1 : +1 range

## Slide 24: Contractive De-Noising Autoencoders (CDAE) for ECG
Xiong et al- 2016 – A stacked contractive denoising auto-encoder for ECG signal denoising
  Used the MIT-BIH Arrhythmia Database for the training and testing sets (samples at 360 Hz) + MIT-BIH noise stress database. Includes baseline wander (BW), muscle artifact (MA), and electrode motion (EM).
  Used a 270->135->70->270 topology and additive noise to model EM interference.
  Reported a 2.40 dB improvement in the Signal to Noise Ratio from current standards (SNRand 0.075-0.350 improvement in the Root Mean Square Error (RMSE=10log)
  https://pdfs.semanticscholar.org/9509/63148f853e0239840ba40bf763e2de24ab37.pdf

## Slide 25: Autoencoders + Fully Connected Network Classifier
AE2
AE3
AE4
AE5
AE1
Z1
Y1
Y1
…
Y255
Y256
310 Input Features
Z2

## Slide 26: Autoencoders + Fully Connected Network Classifier
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Training | 0.5093 | 0.5194 | 0.53301 | 0.5475 | 0.56207 | 0.57747 | 0.59159 | 0.60501 | 0.61819 | 0.62852 | 0.63942
Testing | 0.55859 | 0.44922 | 0.53125 | 0.51172 | 0.5 | 0.5 | 0.50781 | 0.50781 | 0.53516 | 0.47266 | 0.47266
Training Accuracy: 61.82%
Testing Accuracy: 53.52%

## Slide 27: Autoencoders + Fully Connected Network Classifier
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Sensitivity Training | 0.45528 | 0.50466 | 0.51384 | 0.52454 | 0.53876 | 0.552 | 0.56853 | 0.58224 | 0.59882 | 0.61087 | 0.62537
Specificity Training | 0.56332 | 0.53415 | 0.55217 | 0.57047 | 0.58538 | 0.60294 | 0.61465 | 0.62778 | 0.63756 | 0.64617 | 0.65348
Sensativity Testing | 0.59524 | 0.43307 | 0.49612 | 0.45312 | 0.43651 | 0.39844 | 0.44444 | 0.46825 | 0.47656 | 0.44615 | 0.44531
Specificity Testing | 0.52308 | 0.46512 | 0.56693 | 0.57031 | 0.56154 | 0.60156 | 0.57851 | 0.54615 | 0.59375 | 0.5 | 0.5
Training Sensitivity: 59.38%
Training Specificity: 63.76%
Testing Sensitivity: 47.66%
Testing Specificity: 59.38%

## Slide 28: Long Short Term Memory (LSTM) Networks
A2
A3
A4
A5
A1
Z1
Z2
250 Input Features : Five Steps

## Slide 29: Long Short Term Memory (LSTM) Networks
Chart: Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Training | 0.51488 | 0.51912 | 0.53084 | 0.56722 | 0.58987 | 0.60744 | 0.63158 | 0.65065 | 0.67075 | 0.68344 | 0.69544 | 0.70298 | 0.71699 | 0.72978 | 0.74462 | 0.74912
Testing | 0.53125 | 0.59375 | 0.53125 | 0.59375 | 0.34375 | 0.59375 | 0.59375 | 0.71875 | 0.53125 | 0.5 | 0.53125 | 0.46875 | 0.4375 | 0.59375 | 0.59375 | 0.40625
Training Accuracy: 74.46%
Testing Specificity: 59.38%

## Slide 30: Long Short Term Memory (LSTM) Networks
Chart: Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Sensitivity Training | 0.51448 | 0.51876 | 0.52954 | 0.57217 | 0.60698 | 0.6339 | 0.66663 | 0.67938 | 0.69496 | 0.70478 | 0.71495 | 0.72155 | 0.73589 | 0.75034 | 0.77147 | 0.77633
Specificity Training | 0.51528 | 0.51949 | 0.53214 | 0.56227 | 0.57275 | 0.58098 | 0.59653 | 0.62192 | 0.64654 | 0.6621 | 0.67592 | 0.68441 | 0.69809 | 0.70922 | 0.71777 | 0.72192
Sensativity Testing | 0.84776 | 0.054618 | 0.91674 | 0.8031 | 0.19516 | 0.66647 | 0.58678 | 0.926 | 0.30063 | 0.60379 | 0.68049 | 0.61566 | 0.78915 | 0.81 | 0.81613 | 0.79786
Specificity Testing | 0.17198 | 0.95769 | 0.15646 | 0.30867 | 0.90373 | 0.53213 | 0.5057 | 0.15233 | 0.73195 | 0.45285 | 0.3367 | 0.4039 | 0.22397 | 0.21522 | 0.20607 | 0.22501
Training Sensitivity: 77.14%
Training Specificity: 71.78%
Testing Sensitivity: 81.61%
Testing Specificity: 22.50%

## Slide 31: LSTM Networks for ECG Beat Classification
Sucheta et al. – Anomaly Detection in ECG Time Signals via Deep Long Short-Term Memory Networks - 2015
  Used an LSTM network with ECG signal input with training and testing data from the PhysioNet MIT-BIH Arrhythmia Database
  Looked at identifying Premature Ventricular Contraction (PVC), Atrial Premature Contraction (APC), Paced Beats (PB), and Ventricular Couplet (VC)
  http://ieeexplore.ieee.org/document/7344872/
Abnormality | Precision | Recall
Ventricular Couplet | 95.59 | 25.55
Premature Ventricular Couplet | 99.09 | 51.09
Atrial Premature Contraction | 92.31 | 9.53
Paced Beats | 99.30 | 99.86

## Slide 32: LSTM – Lessons Learned
Larger input window per LSTM node with smaller steps
Larger number of hidden nodes (constrained by memory)
Use a smaller batch size ( 32 ) for improved accuracy but longer training time
Initialize the network weights to using random normal distribution
Use the Adam Optimizer (https://arxiv.org/abs/1412.6980)
Soft max with logits for output
Ensure the data is normalized to efficiently use the -1 : +1 range
Use shuffle batch with 100*batch size for capacity
Use balanced data representing disease and non-disease state

## Slide 33: Convolution Network (ConvNet)
Input Signal
1x1250
Convolution Filter
1x48x32
Average Pooling
1x32
Convolution Layer 1
Convolution Filter
1x24x64
Average Pooling
1x16
Convolution Layer 2
X1
B1
X2
…
Xn
Y1
Y2
Fully Connected Layer 3
Output Layer
1024 Nodes

## Slide 34: Convolution Network
Chart: Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Training | 0.86354 | 0.90649 | 0.94285 | 0.95661 | 0.96461 | 0.96688 | 0.97413 | 0.97363 | 0.97516 | 0.97896 | 0.97779 | 0.98176 | 0.9828 | 0.98345 | 0.98547 | 0.98439 | 0.98666 | 0.98792 | 0.9879
Testing | 0.82081 | 0.81952 | 0.82591 | 0.84869 | 0.85649 | 0.87401 | 0.86889 | 0.87713 | 0.88243 | 0.88615 | 0.89799 | 0.90188 | 0.90257 | 0.89534 | 0.92292 | 0.89732 | 0.91725 | 0.91093 | 0.90838
Training Accuracy: 98.55%
Testing Accuracy: 92.29%

## Slide 35: Convolution Network
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Sensitivity Training | 0.86311 | 0.91061 | 0.94522 | 0.95741 | 0.96493 | 0.96578 | 0.9736 | 0.97287 | 0.97386 | 0.97918 | 0.97719 | 0.9817 | 0.98387 | 0.98323 | 0.98583 | 0.98493 | 0.98694 | 0.98869 | 0.98787
Specificity Training | 0.86397 | 0.90237 | 0.94047 | 0.95581 | 0.96429 | 0.96798 | 0.97466 | 0.97439 | 0.97646 | 0.97874 | 0.97838 | 0.98182 | 0.98174 | 0.98366 | 0.9851 | 0.98385 | 0.98637 | 0.98715 | 0.98794
Sensitivity Testing | 0.8411 | 0.83428 | 0.84364 | 0.85323 | 0.85601 | 0.87229 | 0.86788 | 0.87237 | 0.88037 | 0.87751 | 0.89313 | 0.90092 | 0.90104 | 0.89557 | 0.92251 | 0.89967 | 0.91909 | 0.91643 | 0.90777
Specificity Testing | 0.80052 | 0.80475 | 0.80818 | 0.84414 | 0.85696 | 0.87572 | 0.86991 | 0.88189 | 0.88449 | 0.89479 | 0.90284 | 0.90284 | 0.9041 | 0.8951 | 0.92332 | 0.89498 | 0.91541 | 0.90542 | 0.909
Training Sensitivity: 98.58%
Training Specificity: 98.51%
Testing Sensitivity: 92.25%
Testing Specificity: 92.33%

## Slide 36: ConvNet – Lessons Learned
Batch normalization (https://arxiv.org/pdf/1502.03167.pdf)
Reduce the size of kernel and average pooling on each convolution layer
Initialize the network weights to small values in proportion to the nodes in the layer (min , max )
Use the Adam Optimizer (https://arxiv.org/abs/1412.6980)
Soft max with logits for output
Ensure the data is normalized to efficiently use the -1 : +1 range
Use shuffle batch with 100*batch size for capacity
Use balanced data
Use dropout on the fully connected layer
Use ReLU as an activation function

## Slide 37: Deep Learning Classification Results for Atrial Fibrillation
Model | Accuracy - Training | Accuracy - Testing | Sensitivity - Testing | Specificity - Testing
Autoencoder + Fully Connected Neural Network | 61.82% | 53.52% | 59.38% | 47.66%
LSTM | 74.46% | 59.38% | 81.61% | 20.61%
Convolution Network | 98.55% | 92.29% | 92.25% | 92.33%

## Slide 38: Deep Learning Classification Results for Atrial Fibrillation
Chart: 
| Tateno and Glass | Zhou et al | AE + FCNN | LSTM | ConvNet
Sensitivity | 93.2 | 96.89 | 59.38 | 81.61 | 92.25
Specificity | 96.7 | 98.25 | 47.66 | 20.61 | 92.33

## Slide 39: Next Steps
Contractive De-noising Autoencoders (CDAE)
  Remove baseline drift for DC offset, electromagnetic interference (EMI), and muscle artifact
  R-Peak detection for computationally efficient inference for real-time heart rate and heart rate variability

## Slide 40: Next Steps
Convolution Networks
  N-Fold Cross Validation
  Investigate L1 and L2 regularization to improve generalization
AFIB quantification for cardiac ablation surgery decision support.
Investigate other rhythms for cardiac arrhythmia detection (such as Ventricular Tachycardia, Atrial Flutter)
Hybrid network topologies involving CDAE -> ConvNet -> LSTM

## Slide 41: Computing Environment
TensorFlow
NVIDIA GEOFORCE GTX 770M
8 GB RAM
Windows 10
C++ in Microsoft Visual Studio for data preparation

## Slide 42: References
http://www.medicine.mcgill.ca/physio/glasslab/pub_pdf/method_2001.pdf
Goldberger AL, Amaral LAN, Glass L, Hausdorff JM, Ivanov PCh, Mark RG, Mietus JE, Moody GB, Peng C-K, Stanley HE. PhysioBank, PhysioToolkit, and PhysioNet: Components of a New Research Resource for Complex Physiologic Signals. Circulation 101(23):e215-e220 [Circulation Electronic Pages;http://circ.ahajournals.org/content/101/23/e215.full]; 2000 (June 13).
https://www.heartandstroke.ca/heart/conditions/atrial-fibrillation
https://www.cdc.gov/dhdsp/data_statistics/fact_sheets/fs_atrial_fibrillation.htm
http://www.doctoryg.com/2016/10/types-of-atrial-fibrillation.html?spref=pi
https://pdfs.semanticscholar.org/9509/63148f853e023984 0ba40bf763e2de24ab37.pdf
https://biomedical-engineering-online.biomedcentral.com/articles/10.1186/1475-925X-13-18
https://pdfs.semanticscholar.org/9509/63148f853e0239840ba40bf763e2de24ab37.pdf
https://physionet.org/physiobank/database/afdb/
http://ufldl.stanford.edu/tutorial/unsupervised/Autoencoders/
http://blog.fastforwardlabs.com/2016/08/22/under-the-hood-of-the-variational-autoencoder-in.html
http://ieeexplore.ieee.org/document/7344872/
https://pdfs.semanticscholar.org/9509/63148f853e0239840ba40bf763e2de24ab37.pdf
http://www.sciencedirect.com/science/article/pii/S2405818116300538
Adam Optimization: https://arxiv.org/abs/1412.6980
Batch Normalization: https://arxiv.org/pdf/1502.03167.pdf

## Slide 43: Acknowledgements
Dr. Hamid Tazhoosh and the entire Kimia Laboratory (http://kimia.uwaterloo.ca/)
Dr. Ming Li – University of Waterloo
Cloud DX – www.clouddx.com